| Seq. No. | Assessment parameters | Project A of the DRI - 2TDK (investor) | Project B of the Civil initiative (CI) | Remarks by the CI project |
| --- | --- | --- | --- | --- |
|  |  | Single track | Double track | Double track |  |
| 1 | Project documentation: Project for a single track proposed to the supervisor (GEODATA, Milan, Italy) by the DRI (Agency for Infrastructure Development, R Slovenia) a curator of the project; All data by the DRI, acting as a de facto private public company; the investor (2TDK) with the state recapitalization. The general remark of the supervision is negative for the project. The main issues are a lack of suitable protection for the conservation and protected areas, and the overestimated initial economic parameters, which evolved into a considerable overpricing (for some 30 percent). |
| 2 | Preliminary project | At least 17 variants from 1995 till 2009, but only 6 considered for a cross comparison | Preliminary idea from 2017 based on the initial 2001 concept, partially remodelled in 2007-2010; Remark: despite the government’s decision for a double-track railway (June 2017), the prospective planning is indefinite or consumptions | First presented in public in 2016, remodelled in 2017, reconceptualized in 2018 | Preliminary Project B from CI was proposed after when the Project A was public presented. Cost estimation for Project A was in the year 2016 the 1,2 billion EUR without taxis (with taxis was 1,5 billion EUR for single track Cost estimation for project B was 0,8 billion EUR for double track. |
| 3 | Civil Engineering permission | 2016 | Not done | Not done | Many consents can be used from the DRI-2TDK project |
| 4 | Project for erecting | Until 2021 | Not done | Not done | Slovenia has enough capacity for accelerating the project documentation by simultaneously project erecting |
| 5 | Consent from neighbouring country | Done in 2014 for a one-track railway | Not done | Not needed | The new railway was proposed inside the Slovenian territory, away from the international boundaries and the contiguous border-area |
| 6 | The Natura 2000 and infringements of other environmental laws | Infringements of both the national and EU regulations | Not done | The project strictly follows the Natura 2000 prohibitions and restrictions | Main weak point by Project A is Nature 2000 |
| 7 | Main technical characteristics by any project: |
| 8 | Connection with other existing tracks (e.g. international railway to Pula, Istria, Croatia) | The track is out of the existing line and poses additional maintenance costs | Not considered | Can be used supplementary to the existing international railway Divača-Hrpelje/ Kozina-Prešnica-Pula | Construction of the Hrpelje / Kozina junction with the additional inland freight terminal |
| 9 | Total length of the railway | 27,4 km | 27,4 km | 28,2 km |  |
| 10 | Number of critical tunnels | 2 × of 5 km | 3 × 5 km | No tunnel longer than 5 km | 5 km or longer tunnels request special intervention for the fire protection, which was not suitably defined (source: the GEODATA report) |
| 11 | Time travelling | 28 minutes | No data | 20 minutes | Train speed is optimized according the locomotive ability |
| Seq. No. | Assessment parameters | Project A of the DRI - 2TDK (investor) | Project B of the Civil initiative (CI) | Remarks by the CI project |
|  |  | Single track | Double track | Double track |  |
| 12 | Maximal speed | 160 km/h: at 17 ‰ | No data | 120 km/h at 10 ‰, and 80 km/h at 38 ‰ | According to the EU TEN-T standards, up to 40 ‰ (m per km) inclination is allowed in specific geographical circumstances (e.g. Cologne-Karlsruhe, Germany) |
| 13 | Minimal radius of track | 600 m (575 m) | No data | 2800 m | Allows for higher efficiency of the traction force (inertia; pulling/pushing) |
| 14 | Electrical supply | 3 kV, DC | 3kV, DC | 25 kV, 50 Hz/16.6 Hz, AC | CI proposes electrical power supply according the EN 50163. DC power supply is used due to the future TEN-T interoperability conditionality. DRI project used old electrical power supply which has less efficiency and less traction force |
| 15 | Critical points on the line | A curved crossing of a railway bridge underneath the motorway viaduct (high risk of a terrorist attack or sabotage) | A curved crossing of two railway bridges underneath the motorway viaduct (high risk of a terrorist attack or sabotage) | No crossings of considerable defence or security issues | DRI project doesn’t taking into account the military security of terrorists by weak point (viaduct crossing) |
| 16 | Archaeological sites | Some localities from the Roman and Pre-roman period | Some localities from the Roman and Pre-roman period | No trespassing of known or protected archaeological sites | On the DRI project excavation of archaeologists on the plant. |
| 17 | Main financial parameters by a project: |
| 18 | Pre-calculation value of the project | 1,5 billion € | 2,2 to 2,8 billion € | 0,85 billion € | Including the AC power supply station by CI project |
| 19 | Time for construction | 6 to 7 years | 6,5 + 5,5 (consecutive years) = 12 years | 4 to 5 years | Parallel engineering and project realization and project controlling by CI project |
| 20 | Cost mil. € per km | 54,7 mil. € per one-track km | 80,3-102,2 mil. € per two-track km | 29,9 mil. € per two-track km | Cost difference is money for out scope of supply - corruption |
| 21 | Main date at project scheduling: |
| 22 | Start for construction | 2020 | 2026 | 2020 | Construction start for Double track by Project A was not define yet |
| 23 | Public used | 2026 | 2031 | 2025 | Short tunnels allow for shorter construction time |